## Slide 1
Rami Sheikh, and Derek Hower
Efficient Load Value Prediction using Multiple Predictors and Filters

## Slide 2: Executive Summary of Efficient Load Value Prediction
VP #1
VP #3
VP #2
All Load Insts
Value prediction breaks true data dependency
State-of-art VP schemes don’t scale well
w/ VP
IPC = 1
IPC >> 1
Chart: Performance
Component Predictor | 1 | 1 | 1 | 1 | 1
 | 0.01 | 4
Baseline (No VP)
Low ROI
No single VP scheme is capable of predicting all loads efficiently
Increase Budget
Huge Budget
Significant Overlap
Under-utilized Design
Notes: Under-utilized Design  Not all VPs are needed in all apps
Reality: no single predictor is capable of capturing most loads, not efficiently at least
Multi-pred has lots of overlap

## Slide 3: Executive Summary of Efficient Load Value Prediction
Chart: Performance
Component Predictor | 1 | 1 | 1 | 1 | 1
 | 0.01 | 4
Our proposal: a complementary, multi-predictor design
  Eliminate unnecessary overlap
  Improve utilization and storage allocation
  Mitigate pathological behavior
Industry evaluation framework
Results
  Significant performance improvements
  Outperform EVES Predictor (winner of CVP-1)
Smart Training
Hetero. Pred
Predictor Fusion
Accuracy Monitors
Multi-Pred
Best Single Predictor
S: 54%-74%
Compared to EVES VP: 2X Coverage 50% Higher Speedup
Session 6A: INDUSTRY SESSION 2, MICROARCHITECTURE @ 2PM
Notes: Our proposal: a complementary, multi-predictor design + Mitigate pathological behavior using Accuracy Monitors + Eliminate unnecessary overlap with Smart Training + Improve resource allocation using Predictor Fusion + Optimize storage allocation using Heterogenous pred.

## Slide 4: Agenda
Motivation
Methodology
Microarchitecture
Evaluation
Conclusion
Notes: benchmark suites: SPEC2K [38], SPEC2K6 [39], and EEMBC [30].
Moreover, we enriched our benchmark pool with other popular applications:
Linpack [19], media player [23], browser benchmark [4],
and various Javascript benchmarks

## Slide 5: Motivation and Methodology
5

## Slide 6: Motivation
ILP is inherently limited by true data dependencies
 Value Prediction
Remarkable progress towards practical implementation of Value prediction over the past three decades
Costly Mispredictions
Unfortunately, few challenges still need to be addressed …
 Scale up predictor resources
 High Accuracy (>99%)
 Low Coverage
 Predictors scale poorly beyond some point
 Use a multi-predictor design
 Which predictors to use?
 Some predictors are more suitable for predicting certain load patterns
 Challenges: budget, utilization, pathological cases ..etc.
Notes: Our analysis of state-of-art VPs, found that no one predictor is capable of prediction all loads, at least not efficiently

## Slide 7: Methodology
Analyzed loads in 85 workloads
Chart: Breakdown of Dynamic Load Instructions
Pattern-1: Suitable for Last Value Prediction
Pattern-2: Suitable for Stride Address Prediction
Pattern-3: Suitable for Context-based Prediction
Notes: benchmark suites: SPEC2K [38], SPEC2K6 [39], and EEMBC [30].
Moreover, we enriched our benchmark pool with other popular applications:
Linpack [19], media player [23], browser benchmark [4],
and various Javascript benchmarks

## Slide 8: Microarchitecture
8

## Slide 9: Value Prediction
(Optional) On a miss, generate a prefetch
Fetch (multi-cycle)
Decode (multi-cycle)
Rename
Register File Access
Allocate
Update Predictor(s), and Flush on Value Misprediction
Execute
Commit
Issue
Address Prediction
Value Prediction Engine (VPE)
Predicted Address Queue (PAQ)
Fetch Group Address (a proxy for load PC)
If hit and confident
Data Cache
On pipe bubbles
On a hit, return predicted value
❶
❷
❸
❺
❻
Value Prediction
If hit and confident
Filtering Mechanism
Components needed by any value prediction scheme
Components specific to Value Prediction
Components specific to Value Prediction via Address Prediction
addr
value
❹
Two approaches to load value prediction
  Direct: predict the value
  Indirect: predict the address, and read the value from data cache
Preference: direct over indirect
Last VP
Stride AP
Context VP
Context AP
Context Unaware
Context Aware
Direct
Indirect
VTAGE
DLVP
CVP > LVP > CAP > SAP
context-aware over context-unaware
Notes: We prefer:
Direct predictors because they do not require a data cache access, and are not susceptible to cache misses, cache bandwidth constraints, and the increased power of a cache access.
Context-unaware predictors because they are more storage-efficient

## Slide 10: Evaluation Framework
10

## Slide 11: Evaluation Environment
Performance model
  In-house cycle-accurate, RTL-validated, industry simulator
Baseline structures are configured as close as possible to Intel’s Skylake core
  State-of-art TAGE and ITTAGE branch predictors
  Memory dependence predictor similar to Alpha 21264
All of the VPs used are tuned to reach 99% accuracy (see paper for details)
Notes: benchmark suites: SPEC2K [38], SPEC2K6 [39], and EEMBC [30].
Moreover, we enriched our benchmark pool with other popular applications:
Linpack [19], media player [23], browser benchmark [4],
and various Javascript benchmarks

## Slide 12: Results
12

## Slide 13: Performance: Single (Component) vs. Multi-predictor (Composite)
Chart: Predictor Storage (in Kilobytes)
| 2.09375 | 2.40625 | 2.53125 | 4.1875 | 4.8125 | 5.0625 | 8.375 | 9.625 | 10.125 | 16.75 | 19.25 | 20.25 | 33.5 | 38.5
Best Component | 0.021256 | 0.022684 | 0.023797 | 0.025424 | 0.029728 | 0.030829 | 0.032623
Composite | 0.021618 | 0.029447 | 0.035345 | 0.040773 | 0.041377
16%
19%
32%
Composite design trains all predictors
Notes: Preference: LVP > CVP > SAP > CAP

## Slide 14: Observation #1: Pathological Behavior
SAP establishes confidence after observing the same delta 9 times
It takes: 2 iterations to detect stride, and 9 more iterations to get confident
SAP mispredicts 100% of the time!
Solution: Accuracy Monitors (AM)
  Track prediction accuracy, and
  squash prediction if AM indicates prediction unreliable

## Slide 15: Optimization #1: Accuracy Monitors (AM)
Two types of Accuracy Monitors (AM)
  Coarse-grain, epoch based:
    Track number of correct and incorrect confident predictions per predictor  8 counters total
    At end of each epoch:
      For each predictor, compute Mispredictions-per-kilo-prediction (MPKP)
      If MPKP > threshold  predictor goes into training mode (i.e., predictions are not used)
      Counters are reset
  Fine-grain, PC based:
    Use a small, direct mapped, pc indexed/tagged table, with eight counters per entry
    At prediction time:
      On a hit in the table, compute MPKP for each predictor
      If MPKP > threshold  squash the prediction
    Allocation happens on a value misprediction
Chart: Predictor Storage (in Kilobytes)
| 2.09375 | 2.40625 | 2.53125 | 4.1875 | 4.8125 | 5.0625 | 8.375 | 9.625 | 10.125 | 16.75 | 19.25 | 20.25 | 33.5 | 38.5
Composite | 0.021618 | 0.029447 | 0.035345 | 0.040773 | 0.041377
Composite + AM (coarse-grain) | 0.025974 | 0.035855 | 0.042061 | 0.045618 | 0.04789
Composite + AM (fine-grain) | 0.026663 | 0.03534 | 0.045104 | 0.048336 | 0.050689

## Slide 16: Observation #2: Overlap Among Predictors
Chart: 
| One Predictor (LVP) | One Predictor (CVP) | One Predictor (SAP) | One Predictor (CAP) | Two Predictors | Three Predictors | Four Predictors
 | 16.9372 | 11.9324 | 25.008 | 33.7975 | 11.7184 | 0.6059 | 0.00059327
Chart: 
| One Predictor (LVP) | One Predictor (CVP) | One Predictor (SAP) | One Predictor (CAP) | Two Predictors | Three Predictors | Four Predictors
 | 2 | 4 | 20 | 8 | 26 | 11 | 29
Solution: Smart Training (ST)
  If no prediction is made, train all predictors
  If a predictor mispredicted, train it
  Prefers value over address and context-unaware over context-aware: LVP > CVP > SAP > CAP
    Special case: If SAP produced a correct prediction but was not chosen for training, we invalidate the SAP entry
13% by 2+ Predictors
Breakdown of Predicted Loads
66% by 2+ Predictors
Predictors Trained Per Load = 4
Predictors Trained Per Load = 1.1
Notes: If no prediction is made, train all predictors are trained to minimize the amount of time to get a confident prediction. If one or more predictions are made, we only train the predictors that (a) mispredicted, or (b) have the lowest cost according
the heuristic listed below. By always training a component that produced an incorrect prediction, we encourage a quick
eviction of the associated entry (a trained misprediction resets confidence).
Among predictors that produce a correct prediction, we train them in the following order that prefers value over address and context-agnostic over context-aware:
LVP, CVP, SAP, CAP. Additionally, whenever SAP produced
a correct prediction but was not chosen for training, we
invalidate the SAP entry.

## Slide 17: Optimization #2: Smart Training (ST)
Possible Solution: Smart Training Algorithm
  If no prediction is made, train all predictors
  Else if a predictor mispredicted, train it
  Else, prefers value over address and context-agnostic over context-aware: LVP > CVP > SAP > CAP
    If SAP produced a correct prediction but was not chosen for training, we invalidate the SAP entry
Chart: Predictor Storage (in Kilobytes)
| 2.09375 | 2.40625 | 2.53125 | 4.59375 | 4.8125 | 5.0625 | 8.375 | 9.625 | 10.125
Composite + AM | 0.026663 | 0.03534 | 0.045104
Composite + AM + ST | 0.027663 | 0.03734 | 0.049104
Notes: If no prediction is made, train all predictors are trained to minimize the amount of time to get a confident prediction. If one or more predictions are made, we only train the predictors that (a) mispredicted, or (b) have the lowest cost according
the heuristic listed below. By always training a component that produced an incorrect prediction, we encourage a quick
eviction of the associated entry (a trained misprediction resets confidence).
Among predictors that produce a correct prediction, we train them in the following order that prefers value over address and context-agnostic over context-aware:
LVP, CVP, SAP, CAP. Additionally, whenever SAP produced
a correct prediction but was not chosen for training, we
invalidate the SAP entry.

## Slide 18: Observation #3: Under-utilization
Proposed Solutions:
  Predictor Fusion: identify under delivering predictors and re-purpose them
  Heterogenous Predictors
Chart: Breakdown of Dynamic Load Instructions
| zeusmp | lucas | fbital | a2time | cjpeg | typescript
Pattern-1 (Suitable for Last Value Prediction) | 92.9 | 0 | 5.2 | 43.3 | 4.5 | 54
Pattern-2 (Suitable for Stride Address Prediction) | 5.9 | 100 | 0 | 56.6 | 45.2 | 2.9
Pattern-3 (Suitable for Context-based Prediction) | 1.3 | 0 | 94.7 | 0.1 | 50.3 | 43.1
See paper for more details
Predictor Fusion + Heterogenous Predictors
Solutions
Notes: Simplification assumptions: - all VPs has same # of bits/entry
- VPs have same # of entries

## Slide 19: Putting All Pieces Together
Chart: Predictor Storage (in Kilobytes)
| 2.09375 | 2.40625 | 2.53125 | 4.1875 | 4.8125 | 5.0625 | 8.375 | 9.625 | 10.125 | 16.75
MAX (Component) | 0.021256 | 0.022684 | 0.023797 | 0.025424 | 0.029728 | 0.030829
MAX (Composite) | 0.032677 | 0.041482 | 0.049104 | 0.048538
Notes: Simplification assumptions: - all VPs has same # of bits/entry
- VPs have same # of entries

## Slide 20: Comparison Against EVES Predictor (CVP-1 Winner)
EVES: 1st Value Prediction Champion
  Enhanced Vtage Enhanced Stride
Chart: Speedup
| Composite (4.2KB) | Composite (9.6KB) | EVES (8KB) | EVES (32KB) | EVES (Infinite)
Speedup | 0.041482 | 0.048525 | 0.027236 | 0.031273 | 0.031613
Coverage | 42.4999 | 47.9952 | 19.3814 | 20.6376 | 23.4535
> 2X Coverage > 50% Higher Speedup
Composite outperforms EVES in 67 out of 85 workloads, while EVES outperforms in 9 workloads only
Notes: The composite predictor outperforms
EVES in 67 out of 85 workloads, while the latter
outperforms the composite predictor in 9 workloads only

## Slide 21: Conclusions
We advocated a composite predictor design
  Consists of two address and two value predictors
We proposed several optimizations:
  Accuracy Monitors:
    Mitigate pathological behavior
  Smart Training:
    Eliminate unnecessary overlap
  Predictor Fusion:
    Improve utilization
Results
  Significant performance improvements
    Outperforms the best component predictor by 54%-74% depending on predictor size
  Outperform EVES Predictor (winner of CVP-1)
    > 2X Coverage, and > 50% Higher Speedup

## Slide 22: Thank you! Questions?
22

## Slide 23: Backup
23