## Slide 1: PageSeer: Using Page Walks to Trigger Page Swaps in Hybrid Memory Systems
Apostolos Kokolis, Dimitrios Skarlatos and Josep Torrellas
University of Illinois at Urbana-Champaign
http://iacoma.cs.uiuc.edu

## Slide 2: Introduction
Data intensive applications demand memory capacity
DRAM can no longer provide the capacity needed
Non-volatile memory (NVM) technologies
  + higher density
  - slower
Solution: Hybrid Memory Systems
MC
NVM
DRAM
Cannot replace DRAM entirely

## Slide 3: Managing a Hybrid Memory System
DRAM is a cache for the NVM
DRAM and NVM share a flat address space
MC
NVM
DRAM
Capacity loss
More capacity & BW
Need to swap memory
between NVM and DRAM

## Slide 4: Challenges of HW Managed Hybrid Schemes
DRAM
NVM
MC
HW needs to
Swap pages
  Decide which pages to swap
Track page activity
  Accurately identify “hot” pages to swap
Record the page remappings
C
D
F
A
B
Memory Request for Page D
D | 3

## Slide 5: Challenges of HW Managed Hybrid Schemes
DRAM
NVM
MC
A
D
F
C
B
Memory Request for Page C
A | C
HW needs to
Swap pages
  Decide which pages to swap
Track page activity
  Accurately identify “hot” pages to swap
Record the page remappings

## Slide 6: Challenges of HW Managed Hybrid Schemes
DRAM
NVM
MC
HW needs to
Swap pages
  Decide which pages to swap
Track page activity
  Accurately identify “hot” pages to swap
Record the page remappings
Store meta-data information
  Remappings
  Page activity
A
D
F
C
B

## Slide 7: Prior Work
Focused on identifying “hot” pages to swap:
  Use access counters per memory segment
    Conservative swapping  Miss opportunities
  Start a swap on a first access to a memory segment
    Aggressive swapping  Unnecessary traffic
  Predict future memory accesses
    Hard to predict
DRAM
NVM
Swap Buffer
Swap Buffer
Read
Write
Read
Segment ID | Counter
A | 5
B | 4
C | 2
Write
≥ Threshold

## Slide 8: PageSeer Motivation
DRAM
NVM
Swap Buffer
Swap Buffer
Swapping is a costly operation and takes time
Need accuracy in predicting future memory accesses and swapping
Need to start the swaps as early as possible
How to predict future memory accesses?
Read
Read
Write
Write

## Slide 9: PageSeer Motivation
Memory requests require two steps
  Translation from VA to PA
  Data access
TLB
Translation Timeline
CPU
Request
L2
LLC
Memory
PW
PTE
Fill
Caches
Fill
TLB
TLB
Data Access Timeline
Replay CPU
Request
L2
LLC
Memory
L1
TLBs for fast translations
VA to PA address mappings => OS page tables

## Slide 10: PageSeer Motivation
TLB
Translation Timeline
CPU
Request
L2
LLC
Memory
Page
Walk (PW)
Fill
Caches
Fill
TLB
TLB
Data Access Timeline
Replay
Request
L2
LLC
Memory
L1
Memory intensive applications cause TLB misses
TLB miss results in a page walk
If the page is cold
  Page translation
  Actual page data
Miss in caches

## Slide 11: PageSeer Motivation
TLB
Translation Timeline
CPU
Request
L2
LLC
Memory
Page
Walk (PW)
Fill
Caches
Fill
TLB
TLB
Data Access Timeline
Replay
Request
L2
LLC
Memory
L1
At this point we know the page that will be accessed
Insight: Page Walks give information
about future accesses to a page earlier

## Slide 12: Contribution: PageSeer
Uses pages walks to trigger page swaps in HW-only hybrid memory systems
Uses a page-correlation mechanism to prefetch page swaps
Includes HW structures to recognize and move “hot” pages to DRAM
Improves performance by 19% and reduces Average Main Memory Access Time (AMMAT) by 29% over state-of-the-art

## Slide 13: Background – Page Walk
47 - 39 | 38 - 30 | 29 - 21 | 20 - 12 | 11 - 0
c
PUD A
CR3
c
PMD A
c
Physical Address
4-KB Page A
Virtual Address
+
c
PTE A
c
PGD A
+
+
+
+

## Slide 14: PageSeer Design
Core
L1
L2
Shared L3
L1 TLB
L2 TLB
Hybrid Memory Controller (HMC)
MMU
Core
L1
L2
L1 TLB
L2 TLB
MMU
Processor Chip
Path to Memories
DRAM
Crossbar interconnect
Logic Layer
NVM
Logic Layer
Communication link between the MMU and the Hybrid Memory Controller
When a Page Walk reaches the PTE level
  Conventional: MMU sends a memory request to the caches
  PageSeer: in addition MMU sends it to the HMC
Inform the HMC about forthcoming memory accesses

## Slide 15: PageSeer Overview
L2
Shared L3
TLB
MMU
DRAM
NVM
HMC
Data Access Timeline
Translation Timeline
Goal: give time to the HMC for swaps and to prepare its HW structs

## Slide 16: PageSeer Overview
L2
Shared L3
TLB
MMU
DRAM
NVM
HMC
TLB
Data Access Timeline
Replay
Request
L2
LLC
Memory
L1
TLB
Translation Timeline
CPU
Request
L2
LLC
Memory
PW
PTE
Fill
Caches
Fill
TLB
HMC
HMC
1
MMU signals the HMC
HMC finds physical page number
HMC prepares its HW structures
Starts swapping
2
3
A
4
C
PTE

## Slide 17: PageSeer Overview
L2
Shared L3
TLB
MMU
DRAM
NVM
HMC
TLB
Data Access Timeline
Replay
Request
L2
LLC
Memory
L1
TLB
Translation Timeline
CPU
Request
L2
LLC
Memory
PW
PTE
Fill
Caches
Fill
TLB
HMC
HMC
1
MMU signals the HMC
HMC finds physical page number
HMC prepares its HW structures
Starts swapping
2
3
C
4
A
PTE
Benefits:
If the MMU request reaches HMC  PTE is already prefetched
When the request is replayed  page swap to DRAM has already started

## Slide 18: Hybrid Memory Controller
Memory request
PRT
MMU signal
Path to Memories
Hybrid Memory Controller (HMC)
Page Remapping Table (PRT)
Records remappings between DRAM-NVM pages
On the critical path
Every memory request checks the PRT

## Slide 19: Hybrid Memory Controller
Memory request
PRT
MMU signal
Path to Memories
Hybrid Memory Controller (HMC)
Page Remapping Table (PRT)
Hit rate and lookup time is important => Cache some entries
Swap at page granularity
NVM PPN
DRAM PPN
NVM PPN
DRAM PPN
NVM Pages
DRAM Pages
Set 0
Set 1
Set 2
Set 3

## Slide 20: Hybrid Memory Controller
Memory request
PRT
MMU signal
Path to Memories
Hybrid Memory Controller (HMC)
Hot Page Tables (HPTs)
1 for DRAM – 1 for NVM
Track hot pages
DRAM HPT
  Pages that should remain in DRAM
NVM HPT
  Candidate pages to swap to DRAM
Page Number | Counter
HPTs

## Slide 21: Hybrid Memory Controller
Memory request
PRT
MMU signal
Path to Memories
Hybrid Memory Controller (HMC)
HPTs
PCT
PPN | Counter | Next PPN | Next counter
PCT entry
Page Correlation Table (PCT)
Keeps historic data for page accesses
Captures the correlation between pages  prefetch

## Slide 22: Hybrid Memory Controller
Memory request
PRT
MMU signal
Path to Memories
Hybrid Memory Controller (HMC)
HPTs
PCT
MMU Driver
MMU Driver
Receives the MMU signal and checks for prefetch swaps
Receives requests for PTEs
Caches recently fetched PTEs

## Slide 23: Hybrid Memory Controller
Memory request
PRT
MMU signal
Path to Memories
Hybrid Memory Controller (HMC)
HPTs
PCT
MMU Driver
Swap Driver
Initiates page swaps triggered from
  NVM HPT
  PCT
Checks if an access is for a page that is being swapped
Swap Driver

## Slide 24: Evaluation Methodology
Simulator
Simics + SST + DRAMSim2
Modified DRAMSim2 for NVM
Architectures Compared
MemPod [Prodromou ’18]
Workloads
20 benchmarks (SPEC CPU2006, Splash-3 and CORAL)+ 6 mixes of the benchmarks
PoM [Sim ’14]
PageSeer

## Slide 25: Evaluation Parameters
Processor
4 cores @ 2GHz
Memory
1 GHz DDR
HMC
Swap granularity 4KB
DRAM: 512MB, 4 channels
NVM: 4GB, 2 channels
8MB shared L3
PRT and PCT: 32KB, 4-way set associative

## Slide 26: Main Memory Accesses
Chart: Main memory accesses (%)
| PoM | Mempod | PageSeer | PoM | Mempod | PageSeer | PoM | Mempod | PageSeer | PoM | Mempod | PageSeer | PoM | Mempod | PageSeer | SPEC | Splash | CORAL | Mixes | Average
DRAM | 53.1349 | 48.8249 | 81.4209 | 57.3825 | 51.9303 | 89.531 | 55.1335 | 45.0994 | 90.189 | 55.2875 | 46.6894 | 93.8209 | 55.2346 | 48.136 | 88.7404
NVM | 46.8651 | 51.1751 | 16.5936 | 42.6175 | 48.0697 | 9.7675 | 44.8665 | 54.9006 | 5.3165 | 44.7125 | 53.3106 | 4.4187 | 44.7654 | 51.864 | 9.0241
Swap Buffers | 0 | 0 | 1.9855 | 0 | 0 | 0.70148 | 0 | 0 | 4.4945 | 0 | 0 | 1.7605 | 0 | 0 | 2.2355
33%
40%
9%
2%
PageSeer redirects 33% more
memory requests to DRAM
It services read requests from swap
buffers during swaps

## Slide 27: Swap Effectiveness
Chart: Main Memory Accesses (%)
| PoM | Mempod | PageSeer | PoM | Mempod | PageSeer | PoM | Mempod | PageSeer | PoM | Mempod | PageSeer | PoM | Mempod | PageSeer | SPEC | Splash | CORAL | Mixes | Average
Positive | 54.9824 | 59.4828 | 71.0588 | 71.28 | 75.365 | 82.4082 | 70.678 | 72.2616 | 86.9715 | 68.5115 | 69.5534 | 87.1455 | 66.363 | 69.1657 | 81.896
Negative | 3.4943 | 8.8255 | 1.3602 | 2.6608 | 5.3576 | 0.61138 | 8.1827 | 14.9376 | 1.1942 | 6.6811 | 12.272 | 0.87862 | 5.2547 | 10.3482 | 1.0111
Neutral | 41.5233 | 31.6917 | 27.581 | 26.0592 | 19.2774 | 16.9804 | 21.1393 | 12.8008 | 11.8343 | 24.8074 | 18.1746 | 11.9759 | 28.3823 | 20.4861 | 17.0929
12%
15%
1%
PageSeer achieves 12%-15% more
positive memory accesses because of
swaps and only 1% negative accesses
5%
10%
Positive
Access DRAM thanks to a swap
Negative
Access NVM due to a swap
Neutral
Access DRAM or NVM as if no swap happened

## Slide 28: Types of swaps
Prefetching-Triggered: Aggressive swaps triggered by the Page Correlation Table based on historic access patterns
  MMU-Triggered: Subset of Prefetching Triggered directly initiated by the MMU
HPT-Triggered: Conservative swaps triggered by the NVM Hot Page Table when accesses to a page reach a threshold

## Slide 29: Swap Characterization
Chart: Number of Swaps (%)
| bwaves | mcf | fft | luCon | luNCon | LULESH | lbm | milc | GemsFDTF | libquantum | omnetpp | leslie3d | radix | oceanCon | barnes | stream | miniFE | AMGmk | SNAP | MILCmk | mix1 | mix2 | mix3 | mix4 | mix5 | mix6 | Average
Prefetching-Triggered | 6.7116 | 11.2745 | 0.90287 | 4.5728 | 30.2326 | 16.1987 | 99.756 | 78.9115 | 67.3964 | 99.9736 | 53.3388 | 87.5544 | 75.18 | 65.8809 | 57.5874 | 99.9721 | 99.9766 | 98.1956 | 70.8751 | 99.966 | 63.0442 | 77.5058 | 76.9544 | 82.6864 | 43.6861 | 65.4282 | 62.837
HPT-Triggered | 93.2884 | 88.7255 | 99.0971 | 95.4272 | 69.7674 | 83.8013 | 0.24402 | 21.0885 | 32.6036 | 0.026374 | 46.6612 | 12.4456 | 24.82 | 34.1191 | 42.4126 | 0.027874 | 0.023416 | 1.8044 | 29.1249 | 0.033993 | 36.9558 | 22.4942 | 23.0456 | 17.3136 | 56.3139 | 34.5718 | 37.163
filler 1
filler 2
MMU-Triggered | 4.4076 | 0.40369 | 0.0040064 | 1.7453 | 27.907 | 11.7506 | 91.3539 | 56.4985 | 42.7933 | 51.5172 | 44.7908 | 15.5845 | 69.4028 | 51.4572 | 42.4777 | 78.4445 | 75.5811 | 83.2886 | 58.6586 | 89.672 | 58.8953 | 69.9296 | 67.666 | 69.5142 | 40.6386 | 59.2753 | 48.6022
49%
63%
37%
Most of the swaps are Prefetching swaps
Most Prefetching swaps are MMU swaps

## Slide 30: Swap Characterization
Chart: Number of Swaps (%)
| mcf | fft | luCon | lbm | stream | miniFE | AMGmk | MILCmk | mix2 | mix3 | mix4 | Average
Prefetching-Triggered | 11.2745 | 0.90287 | 4.5728 | 99.756 | 99.9721 | 99.9766 | 98.1956 | 99.966 | 77.5058 | 76.9544 | 82.6864 | 62.837
HPT-Triggered | 88.7255 | 99.0971 | 95.4272 | 0.24402 | 0.027874 | 0.023416 | 1.8044 | 0.033993 | 22.4942 | 23.0456 | 17.3136 | 37.163
filler 1
filler 2
MMU-Triggered | 0.40369 | 0.0040064 | 1.7453 | 91.3539 | 78.4445 | 75.5811 | 83.2886 | 89.672 | 69.9296 | 67.666 | 69.5142 | 48.6022

## Slide 31: Swap Characterization
Chart: Number of Swaps (%)
| mcf | fft | luCon | lbm | stream | miniFE | AMGmk | MILCmk | mix2 | mix3 | mix4 | Average
Prefetching-Triggered | 11.2745 | 0.90287 | 4.5728 | 99.756 | 99.9721 | 99.9766 | 98.1956 | 99.966 | 77.5058 | 76.9544 | 82.6864 | 62.837
HPT-Triggered | 88.7255 | 99.0971 | 95.4272 | 0.24402 | 0.027874 | 0.023416 | 1.8044 | 0.033993 | 22.4942 | 23.0456 | 17.3136 | 37.163
filler 1
filler 2
MMU-Triggered | 0.40369 | 0.0040064 | 1.7453 | 91.3539 | 78.4445 | 75.5811 | 83.2886 | 89.672 | 69.9296 | 67.666 | 69.5142 | 48.6022
In every case PageSeer maintains
high performance

## Slide 32: Performance Speedup
Chart: Speedup
| SPEC | Splash | Coral | Mixes | Average
Mempod | 1 | 1 | 1 | 1 | 1
PoM | 1.0953 | 0.9908 | 1.1505 | 1.0539 | 1.0726
PageSeer | 1.2729 | 1.1403 | 1.5043 | 1.2225 | 1.285
19%
28%
Reduces AMMAT by 37% and 29%
Improvement is mainly due to:
  Swaps
  Less time spent at the PRT (~62% less)

## Slide 33: Also in the paper . . .
More details on PageSeer
  Operation
  Power and area numbers for the HMC hardware structures
Swap accuracy, page walk requests and swap characterization
How to utilize the swap buffers during the swap process

## Slide 34: Conclusion
PageSeer uses page walks and correlation prefetching to trigger page swaps accurately and promptly
MMU hints help to identify future memory accesses; start swaps and prepare the HMC hardware structures
PageSeer improves IPC by 19% and reduces AMMAT by 29% over prior state-of-the-art schemes

## Slide 35: PageSeer: Using Page Walks to Trigger Page Swaps in Hybrid Memory Systems
Apostolos Kokolis, Dimitrios Skarlatos and Josep Torrellas
University of Illinois at Urbana-Champaign
http://iacoma.cs.uiuc.edu
HPCA 2019
Session 8A: MEMORY
Thank you!!

## Slide 36: BACKUP SLIDES
Average: 87% accuracy

## Slide 37: BACKUP SLIDES
Average: 62% PRT reduction

## Slide 38: BACKUP SLIDES
0.35 to 0.19 swaps per KInst
15% PTE cache misses

## Slide 39: END